## Slide 1: Ingress firewall implementation FreeRTOS
Politecnico di Torino:
Computer Architecture and
Operating Systems course:
2023/2024
Group 5:
Michele Seira, Fardo Giorgio, Luca Ponzo, Gianfranco Trad

## Slide 2
Project intent: create a working firewall for FreeRTOS
Requirements :
  Function entry points for filtering packets
  Handling of rejected packets
    Print to stderr
  Rule generation
    YAML to C struct
  Rule storage
    Inline C structs in rules.h
  (WIP) integration with IDS
    Snort

## Slide 3: Understanding FreeRTOS IP stack : Packet processing pipeline

## Slide 4: Functions
FreeRTOS_IP.c:prvProcessIPPacket
FreeRTOS_IP.c:checkPacketAgainstRules
FreeRTOS_IP.c:checkIPs & checkPacketsWithPort
packet interception point

## Slide 5: Handling of rejected packets
FreeRTOS_IP.c:writeToPcap
Python .log to PCAP conversion function
write the data of the rejected packets in stderr
  marking every rejected packet with #PCAP
pipe the qemu-system-arm output, that is all directed to stderr, to a file out.log
process the file to compile a pcap

## Slide 6: Rules generation Rules storage
FreeRTOS-Plus-TCP/rules.h:
rules.yaml

## Slide 7: Tests for rules and output PCAP
Packet generation calls that are fed to scapy : 6 packets 3 of which are expected to be rejected by the rules defined earlier
The 3 rejected packets as expected

## Slide 8: Integration of IDS
Rules defined to monitoring only the ICMP packets through SNORT, only proof of concept needs more work
preliminary work for POC using SNORT to process rejected packets by the firewall
needs second NIC or SNORT endpoint with TCP retransmission mechanism

## Slide 9: Thanks !
And now time for the live demo 🙅